## Slide 1: Application of proton activation analysis to determine the lithium content in samples.
A.Aleksanyan, S.Amirkhanyan, A.Aperyan, H. Gulkanyan, V.Ghavalyan, T. Kotanjyan, L. Poghosyan, A. Sahakov, A. Shahinyan
“A. I. Alikhanyan national science laboratory ( Yerevan Physics Institute ) ” (AANL)
“Neutron Physics and Radiation Materials” Conference, October 27–30, 2025, Yerevan

## Slide 2: AANL installations for conducting scientific and applied research.
Cyclotron C-18 Ep = 18 MeV, Ip=1-30 mkA.
Linear electron accelerator (LINAC-75) Ee = 10 to 75 MeV, Ie = up to 1 mkA.
Low-background setup based on an HPGe GCD-20180 high-purity germanium detector․ The laboratory is located in the Avan salt mine at a depth of 650 meters of water equivalent.

## Slide 3
The presence of a cyclotron, electron accelerator, and unique underground laboratory at the AANL allows not only to conduct research on rare nuclear processes but also to solve applied problems in the fields of ecology, medicine, geology, metallurgy, and mineral exploration.
It is especially important to note the presence of a low-background installation based on a lead-shielded HPGe detector in the AANL underground laboratory.

## Slide 5
The number of background events registered by the HPGe detector within an hour (a) – in ground-based measurements, (b) – in underground measurements with protection.

## Slide 6
The importance of rare and rare earth metals has increased dramatically. Therefore, determining the quantitative composition of these metals in rocks and processed waste is becoming increasingly important for responsible mining and processing methods.
The methods of proton activation and gamma activation analysis we use are aimed at determining the quantitative composition of such metals.

## Slide 7
When targets from the studied sample are irradiated with protons or gamma quanta, daughter isotopes of the elements present in the sample are formed as a result of proton-nuclear and photonuclear reactions.
As a result of gamma-spectrometric analysis, based on the measured induced activity of characteristic γ-radiation, it is possible to determine the number of nuclei of the parent isotope present in the target and, thereby, the number of nuclei of the desired chemical element present in the target.

## Slide 8
Studies have shown that proton activation and gamma activation analysis methods can simultaneously determine the quantitative composition of dozens of elements in a sample, while having different concentrations.
At the AANL linear electron accelerator, using bremsstrahlung photon beams, gamma-activation analysis (GAA) of geological obsidian samples was carried out for the first time in Armenia.

## Slide 9
The results of the analysis of a number of chemical elements in an obsidian sample were shown to be comparable to the results of instrumental neutron activation analysis (INAA) of the same sample, conducted at the Center for Archaeometry Mainheim, Germany, after irradiation with neutrons in the specialized TRIGA nuclear reactor at the Institute of Nuclear Chemistry at the University of Mainz.
Using the GAA method, it is possible to obtain data on the content of elements (Ca, Ti, Mn, Sr, Y, Nb, Mo, Pb), for which the INAA method was ineffective.

## Slide 10: Advantages of proton activation and gamma activation analysis methods.
Gamma-spectrometry analysis was carried out using a low-background setup based on an HPGe detector located in the AANL underground laboratory.
The setup provides high resolution and is protected by a shield made of high-purity lead and copper.
The energies of the characteristic gamma quanta accompanying the beta decays of daughter nuclei obtained as a result of irradiation are in a wide range (80 keV – 3000 keV)
A significant fraction of the daughter nuclei formed as a result of irradiation of the elements of interest have suitable and at the same time different half-lives Т½.
The elements being studied have isotopes and, accordingly, as a result of various reactions (γ, n), (p, n), several daughter radioactive nuclei are formed.
Samples do not require pre-treatment.
Both methods complement each other.

## Slide 11
This report is devoted to the possibility of determining the content of one of the rare metals, namely lithium (Li), in a sample using proton activation analysis.
Lithium's properties and characteristics, including its high energy density, low density, high electrochemical potential, and abundance in the Earth's crust, make it a critical element for a variety of industrial applications, particularly in batteries, electronics, automotive, and aerospace.

## Slide 12: Schematic diagram of a target system for the quantitative determination of lithium (Li) content in a sample using a proton beam.
Proton energy Ep =18 MeV.
Proton beam current Ip = 1.0 mkA.
Irradiation time is 10 minutes.
StSt – duct window – stainless steel d=100 µm.
Airspace – air space L=13 cm,
Cu – monitor - copper foil d=25.4 µm
LiF – lithium fluoride
Grave – rock sample
Al – aluminum foil d=20 µm
Cu
Cu
LiF
StSt
Cu
LiF
LiF
Al
Cu
Grave
Cu
LiF
Cu
Airspace L=13 cm

## Slide 13: Gamma spectrometric analysis was carried out using a low-background setup based on an HPGe detector located in the underground laboratory of the Avan salt mine.
As a result of spectrometric analysis, the yield Y (the number of nuclei of a given radioisotope formed as a result of irradiation per unit of time) of the radioisotope is determined.
where S is the area of the total absorption photopeak,
Iγ is the relative intensity of the γ-line,
εγ is the γ-ray detection efficiency,
λ is the decay constant of the given radioisotope,
tp – is the irradiation time,
tc – cooling time,
tR and tL are the real and live time of the γ-spectroscopic measurement

## Slide 14: Copper targets were used to determine the proton beam current in different targets by measuring the yield of the monitor reaction 65Cu(p,n)65Zn
Chart: σm (mb) 65Cu(p,n)65Zn

## Slide 15
The data on the cross section σm(Ep) of the reaction 65Cu(p,n)65Zn recommended by the IAEA were used.
The energy spectra fp (Ep) of protons incident on each target were calculated using the SRIM/TRIM and GEANT programs.
As a result of convolution of the given spectra, we obtain the cross section of the 65Cu(p,n)65Zn reaction for each monitor target.
σ mi = ∫ σm(Ep)·f(Ep )·dEp

## Slide 16
The yield values (Ymi) and the corresponding cross-sections (σmi) of irradiated copper foils obtained as a result of gamma-spectroscopic analysis make it possible to estimate the proton beam current I pi (i=1..6) in each copper foil.
I pi = Ymi / (νmi x σ mi )
νm – surface density of target nuclei cm-2
NA – Avogadro's constant, Am – atomic mass, fm - relative abundance of a given isotope

## Slide 17: Estimation of the cross section of the 7Li(p,n)7Be reaction occurring as a result of irradiation in each LiF target.
Gamma-spectroscopic analysis of irradiated LiF samples identified the 7Be nucleus by detecting the accompanying beta decay, a characteristic gamma quantum with an energy of Eγ = 477.6 keV (Iγ = 10.44%). The reliability of the identification was verified by comparing the half-life of 7Be with the obtained value T1/2 = 54.2 ± 2.4 days.
For each LiF sample, the yield (Ymi) of the radioisotope 7Be was calculated using gamma-spectroscopic analysis.
Using the values ​​of the proton beam currents passing through the copper foils, the cross sections of the 7Li(p,n)7Be reaction can be estimated for each LiF target.
σ LBi = YBei / (νLii x I i )

## Slide 18: Parameters of experimental targets, characteristics of the proton beam, and results of measuring the cross section of the 7Li(p,n)7Be reaction.
 | Subtarget and Thickness or mass | <Ep> (MeV) | σLi (mb) 7Li(p,n)7Be | Y (in 106/sec) | Ip (in µA)
1 | Cu1 d=25.4 µm, m= 0,0232g | 16.05±0.17 |  | 11.48±0.96 | 0.234±0.019
2 | LiF1 d=107 µm, m= 0,034g | 15.54±0.28 | 31.34±3.43 | 31.73±2.18 | 0.226±0.019
3 | Cu2 d=25.4 µm, m= 0,0225g | 14.50±0.19 |  | 17.61±1.75 | 0.216±0.021
4 | LiF2 d=119 µm, m= 0,034g | 13.96±0.31 | 36.78±4.07 | 33.81±2.49 | 0.201±0.019
5 | Cu3 d=25.4 µm, m= 0,0222g | 12.69±0.21 |  | 26.98±2.16 | 0.194±0.016
6 | LiF3 d=117 µm, m= 0,034g | 12.17±0.37 | 42.96±5.0 | 34. 25±2.58 | 0.181±0.017
7 | Cu 4 d=25.4 µm, m= 0,0232g | 10.78±0.44 |  | 34.73±2.83 | 0.171±0.012
8 | Gr m=0.0402g mLi in Qaj =34.01±5.35mg/kg | 9.93±0.26 | 66.93±7.2 | (8.45±2.61)*103 | 0.198±0.015
9 | Cu5 d=25.4 µm, m= 0,0205g | 7.28±0.30 |  | 32.56±2.37 | 0.287±0.026
10 | LiF4 d=125 µm, m= 0,0331g | 6.25±0.38 | 129.7±26.3 | 104.54±7.22 | 0.168±0.032

## Slide 19: Cross section of reaction 7Li(p,n)7Be

## Slide 20: Experimental results
The cross-section values ​​for the 7Li(p,n)7Be reaction in the region Ep = 8-15 MeV were obtained. The obtained values ​​were compared with data available in the literature.
The lithium (Li) content in the sample was calculated: mLi = 34.01±5.35 mg/kg

## Slide 21: Schematic diagram of a target system for the quantitative determination of lithium (Li) content in a salt ore sample using a proton beam.
Proton energy Ep =18 MeV.
Proton beam current Ip = 1.0 mkA.
Irradiation time is 10 minutes.
StSt – duct window – stainless steel d=100 µm.
Airspace – air space L=13 cm,
Cu – monitor - copper foil d=25.4 µm
LiF – lithium fluoride
HH1, HH2 – salt ore samples
Al – aluminum foil d=20 µm
Cu
Cu
HH1
StSt
Cu
LiF
LiF
Al
Cu
HH2
Cu

## Slide 22: Parameters of experimental targets, characteristics of the proton beam, and results of measuring the cross section of the 7Li(p,n)7Be reaction.
 | Subtarget and Thickness or mass | <Ep> (MeV) | σ Li (mb) | Ym (in 106/sec) | Ip in µA)
1 | Cu1 d=25.4 µm, m= 0,0389g | 16.07±0.25 | 152,68 | 14.09±0.96 | 0.223±0.016
2 | HH1 m= 0,209g | 15.54±0.26 |  |  | 0.197±0.029
3 | Cu2 d=25.4 µm, m= 0,0385g | 11.63±1.0 |  | 37.34±2.53 | 0.171±0.019
4 | LiF1 m= 0,058g m Li1 = 0.015 g | 10.80±0.84 | 68.06±7.2 | 61.74±3.93 | 0.168±0.014
5 | Cu3 d=25.4 µm, m= 0,0414g | 9.36±0.88 |  | 32.64±2.36 | 0.165±0.019
6 | HH2 mLi HH2 = 1.73x 10-5 g 100.6±12.6 mg/kg, mLi HH2 = 93.5±4.8 mg/kg, m Li HH2 = 112.6±9.7 mg/kg | 8.33±1.07 | 92.6±11.1 99.0±5.1 | 82751±6197 | 0.161±0.016
7 | Cu4 d=25.4 µm, m= 0,0443g | 7.48±1.20 |  | 12.85±0.91 | 0.157±0.021
8 | LiF2 m= 0,0413g m Li2 = 0.011 g | 7.14±0.88 | 103.2±17.4 | 45.67±2.53 | 0.125±0.019

## Slide 23: The lithium (Li) content in the HH2 salt ore sample was calculated using three methods.
Express method
m Li HH2 = 112.6±9.7 mg/kg.
Using the above method
m Li HH2 =100.6±12.6 mg/kg.
Using the cross-section value from the literature mLi HH2 = 93.5±4.8 mg/kg.

## Slide 24
γ-spectra of sample HH2 after 8 and 29 days of irradiation, respectively.

## Slide 25: Schematic diagram of the target system for determining the quantitative content of lithium (Li) in a reference sample of granite grade N42 MK-4 using a proton beam.
Proton energy Ep = 18 MeV
Proton beam current Ip = 1.1 mkA.
Irradiation time is 10 minutes.
StSt – duct window – stainless steel d=100 µm.
Airspace – air space L=14 cm,
Cu – monitor - copper foil d=25.4 µm
N42 – reference sample of granite grade N42 MK-4
Al – aluminum foil d=20 µm
The lithium content was calculated for granite sample N42-2
m Li N42-2 = 28.35 ±4.2 mg/kg
Cu
Cu
N42
StSt
Cu
N42
N42
Al
Cu
Cu
N42
Cu
Airspace L=14cm
N42

## Slide 27: Conclusion
The lithium (Li) content of geological samples taken from a mine in southern Armenia and from the Avan salt mine (Yerevan) was determined to be 34.0 ± 5.3 mg/kg and 100.6 ± 12.6 mg/kg, respectively.
The reliability of the proton activation analysis method was verified by comparing the previously known lithium (Li) content in the reference sample of granite grade N42 MK-4 (26 mg/kg) with the value of 28.35 ±4.2 mg/kg measured in this work.

## Slide 28: THANK YOU FOR YOUR ATTENTION

## Slide 33
Target-core | Isotope fraction of an element % | reaction under study | the daughter nucleus of the (p,X) reaction and its half-life | The energy (keV) and intensity of the γ-quantum accompanying (%) the fission of the daughter nucleus
192Os | 40.78 | 192Os(p,n)192Ir | 192Ir (73.829 օր) | 316.506(82.86%)
190Os | 26.26 | 190Os(p,n)190Ir | 190Ir (11.78 օր) | 605.14 (37.8%)
103Rh | 100 | 103Rh(p,d) 102Rh | 102Rh (207.3 օր) | 475.06 (46.0%)
105Pd | 22.33 | 105Pd(p,n) 105Ag | 105Ag (41.29 օր) | 344.61 (42.0%)
197Au | 100 | 197Au(p,n) 197Hg | 197Hg (23.8 ժամ) | 134(33%), 279.0(6%)
196Pt | 25.21 | 196Pt(p,n)196Au | 196Au (6.1669 օր) | 333.03 (22.9%) 355.73(87.0 %)
45Sc | 100 | 45Sc(p,p+n)44Sc 45Sc(p,p+n)44mSc | 44Sc (4.042 ժամ) 44mSc (58.61 ժամ) | 1157.022(99.887%) 271.251(86.72%)
89Y | 100 | 89Y(p,n)89Zr | 89Zr (78.41 ժամ) | 909.15 (99.04%)
89Y | 100 | 89Y(p,2n)88Zr | 88Zr (83.4 օր) | 392.87 (97,29%)
139La | 25.21 | 139La(p,n)139Ce | 139Ce (137.64 օր) | 165.87 (79.9%)
140Ce | 88.45 | 140Ce(p,d)139Ce | 139Ce (137.64 օր) | 165.87 (79.9%)
142Ce | 11.11 | 142Ce(p,d)141Ce | 141Ce (32.504 օր) | 145.44 (48.3%)
Some characteristics of (p,X) reactions for determining the content of precious and rare earth metals

## Slide 34
144Nd | 23.798 | 144Nd(p,n)144Pm | 144Pm (363 օր) | 618.01 (98.0%)696.49(99.49%)
148Nd | 5.756 | 148Nd(p,n)148Pm 148Nd(p,n)148Pm | 148Pm (5.368 օր) 148Pm (41.29 օր) | 550.27 (22.0%) 550.27(94.9%)629.97(89.0%)
144Nd | 23.798 | 144Nd(p,n)144Pm | 144Pm (363 օր) | 618.01 (98.0%)696.49(99.49%)
147Sm | 15 | 147Sm (p,n)147Eu | 147Eu (24.1 օր) | 197.299 (24.08%)677.52(9.8%)
151Eu | 47.81 | 151Eu (p,n)151Gd | 151Gd (124.5 օր) | 153.6 (6.2%) 243.29 (5.6%)
156Gd | 20.47 | 156Gd (p,n)156Tb | 156Tb (5.35 օր) | 534.29 (67%) 1222.44 (31%)
168Er | 26.978 | 168Er (p,n)168Tm | 168Tm(93.1 օր) | 198.25 (54.49%) 815.99 (50.95%)
169Tm | 100 | 169Tm(p,d)168Tm | 168Tm(93.1 օր) | 198.25 (54.49%) 815.99 (50.95%)
169Tm | 100 | 169Tm(p,n)169Yb | 169Yb (32.015օր) | 177.21 (22.28%)197.957(35.93%)
172Yb | 26.978 | 172Yb(p,n)172Lu | 172Lu (6.70օր) | 900.72 (29.8%)1093.63(63.0%)
175Lu | 97.401 | 175Lu (p, n)175Hf | 175Hf (70.67 օր) | 343.40 (84%)

## Slide 35
Target-core | Isotope fraction of an element % | reaction under study | the daughter nucleus of the (γ,X) reaction and its half-life | The energy (keV) and intensity of the γ-quantum accompanying (%) the fission of the daughter nucleus
103Rh | 100 | 103Rh(γ,n) 102Rh | 102Rh (207.3 օր) | 475.06 (46.0%)
106Pd | 27.33 | 106Pd(γ,p) 105Rh | 105Rh (35.34 ժամ) | 319.23 (16.9%)
197Au | 100 | 197Au(γ,n) 196Au | 196Au (6.1669 d) | 355.68 (87%)
198Pt | 7.356 | 198Pt(γ,n) 197Pt | 197Pt (19.89 ժամ) | 191.437(3.7 %)
45Sc | 100 | 45Sc(γ,n)44Sc 45Sc(γ,n)44mSc | 44Sc (4.042 ժամ) 44mSc (58.61 ժամ) | 1157.022(99.887%) 271.251(86.72%)
89Y | 100 | 89Y(γ,n)88Y | 88Y (106.627 օր) | 898.04 (93.7%) 1836.06 (93.7%)
89Y | 100 | 89Y(γ,2n)87Y | 87Y (79.8 ժամ) | 388.53 (82,2%) 484.805 (89,8%)
140Ce | 88.45 | 140Ce(γ,n)139Ce | 139Ce (137.64 օր) | 165.87 (79.9%)
142Ce | 11.11 | 142Ce(γ,n)141Ce | 141Ce (32.504 օր) | 145.44 (48.3%)
Some characteristics of (γ,X) reactions for determining the content of precious and rare earth metals

## Slide 36
140Ce | 88.45 | 140Ce(γ,n)139Ce | 139Ce (137.64 օր) | 165.87 (79.9%)
142Ce | 11.11 | 142Ce(γ,n)141Ce | 141Ce (32.504 օր) | 145.44 (48.3%)
148Nd | 5.756 | 148Nd(γ,n)147Nd | 147Nd (11.12 օր) | 531.01 (13.11%)
160Gd | 21.86 | 160Gd(γ,n)159Gd | 159Gd (18.479 ժամ) | 363.54 (11.78%)
159Tb | 100 | 159Tb(γ,3n) 156Tb | 156Tb (5.35 օր) | 534.29 (67%) 1222.44 (31%)
169Tm | 100 | 169Tm(γ,n)168Tm | 168Tm(93.1 օր) | 198.25 (54.49%) 815.99(50.95%)
176Yb | 12.996 | 176Yb(γ,n) 175Yb | 175Yb(4.185 օր) | 396.329 (13.2%)
175Lu | 97.401 | 175Lu(γ,3n)172Lu | 172Lu (6.702 օր) | 900.724 (29.8%) 1093.63 (63%)

## Slide 37
Elements | Relative content of an element (µg/g or %) measured by the GAA method | Relative content of an element (µg/g or %) measured by the INAA method
Na (%) | 2.520.33 | 3.22
K (%) | 3.790.35 | 3.40
Ca (%) | 0.445 0.043 | Нет данных
Sc | 3.2 0.6 | 2.50
Ti (%) | 0.0700.004 | Нет данных
Cr | 3.5 2.7 | 6.00
Mn | 40429 | Нет данных
Fe (%) | 0.580.06 | 0.61
Co | 1.590.60 | 1.09
Zn | 47.815.5 | 40.0
As | 2.53 0.36 | 5.10
Rb | 1288 | 135
Sr | 32.32.7 | Нет данных
Y | 26.31.9 | Нет данных
Zr | 72.25.1 | 73
Nb | 32.72.1 | Нет данных
Mo | 6.11.0 | Нет данных
Sb | 1.00.3 | 0.16
Cs | 3.570.24 | 3.64
Ва | 40548 | 388

## Slide 38
Се | 48.66.6 | 40.4
Nd | Нет данных | 17.0
Sm | Нет данных | 3.42
Eu | Нет данных | 0.369
Tb | Нет данных | 0.57
Yb | Нет данных | 2.44
Lu | Нет данных | 0.480
Hf | Нет данных | 3.45
Ta | Нет данных | 1.97
Pb | 16.12.8 | Нет данных
Th | 20.42.4 | 16.3
U | 5.740.45 | 6.20

## Slide 39
Apple-ում օգտագործվում են
Gd
Y
Dy
Eu
La
Nd
Pr
Tb
Ce

## Slide 40
Sc, Dy, Gd, Tb, Lu, Sm, Y - արգելք

## Slide 41: Ծանր մետաղների և մետալոիդների դասակարգումը 3 վտանգի դասերի
Վտանգի դաս | ГОСТ 17.4.02.-83 Ռուսաստան | RIVM Report Netherlands
Հատկապես թունավոր | As Cd Hg Se Pb Zn | Be Se Tl Sb Cd
Թունավոր | Co Ni Mo Cu Sb Cr | V Hg Ni Cu Cr As Ba
Ցածր թունավորության | Ba V W Mn Sr | Zn Co Sn Ce Pb Mo

## Slide 43
Տարր | Տարրի տարածվածությունն ըստmզանգվածի -% կամ մկգ/գ | Տարրի տարածվածությունն օբսիդիանում ըստ զանգվածի -% մկգ/գ | Տարրի տարածվածությունն գռանոդիարիտ ըստ զանգվածի -% մկգ/գ | SRM 278 INAA
O | 49.13 |  |  | 
Si | 27.5 |  | 30.3 | 36.6
Al | 7.45 |  | 8.8 | 7.8
Fe | 4.2 | 0.580.06 | 3.25 | 1.32
Ca | 3.2 | 0.445 0.043 | 2.75 | 0.60
Na | 2.4 | 2.520.33 | 3.16 | 
K | 2.35 | 3.790.35 | 2.59 | 3.44
Ti | 0.61 | 0.0700.004 | 0.38 | 
Mn | 1000 | 40429 |  | 430
Ba | 500 | 40548 | 970 | 1072
Sr | 360 | 32.32.7 | 500 | 
Rb | 110 | 1288 | 121 | 129.3
Y | 28 | 26.31.9 | 25 | 
Zr | 16 | 72.25.1 | 230 | 208
Nb | 10 | 32.72.1 | 15 |